PAKISTAN AERONAUTICAL COMPLEX, KAMRA

AVIONICS PRODUCTION FACTORY

TENDER NOTICE NO: APF/1920/42/LOG/PC-70       DATED                      22 MARCH, 2021

1.	SEALED TENDERS FROM PAC BOARD REGISTERED FIRM FOR PURCHASE OF UNDERMENTIONED ITEMS ARE INVITED.

| S NO | PART NO | NOUN | U/I | QTY | SPECIFICATION |
| --- | --- | --- | --- | --- | --- |
| 1 | DS700PCEL | SOLDERING STATION | EA | 01 | Model : WD1MN or Equivalent Brand : Weller or Equivalent Wattage : 160W Temperature Range : 150 to 850 °F Voltage Input : 120V Voltage output : 24V Accessories Type :- WMRS Solder Pencil with stand WMRT Desoldering Tweezers with stand 05 extra bits |
| 2 | HP8482A | POWER SENSOR -30dBm TO +20dBm (1pW-100mW) Frequency range 100KHz -4.2GHz | EA | 01 | Model : HP8482A or Equivalent Power Range : -30 dBm to +20 dBm (1 µW to 100 mW) Frequency Range : 100kHz to 4.2GHz Nominal Impedance : 50Ω Maximum Power : 300 mW Maximum Peak Power : 15 W Peak Maximum Energy / Pulse: 30 W. µs RF Connector : Type N Male (75Ω) |
| 3 | 44-39-150 | SOLDERING STATION | EA | 01 | Model : WE1010NA or Equivalent Brand : Weller or Equivalent Wattage : 70W Temperature Range : 200 to 850 °F Voltage Input : 120V Voltage output : 23V Accessories Type :- WE1 Station 120V WEP70 Soldering Iron 70W 23V with stand PH70 safety rest ETA tip 0.062" / 1.6mm screwdriver with all types of ET soldering tips e.g. screwdriver tip Qty-02 Long screwdriver tip Qty-02 Narrow screwdriver tip Qty-02 Conical tip Qty-02 Long Conical tip Qty-02 Single Flat tip Qty-02 Knife tip Qty-02 |
| 4 | 5844NL-OPS-CONCOLE-MPDR-90 | CONSOLE WITH SLIDE PANEL | EA | 01 | Console Dimensions (30"x30"x18") Slide Panel Dimensions (9"x3.5"x18") Console Frame Dimensions (26.4"x17.6") |
| 5 | CFSL-687CB | SCREEN FLUXPORTABLE ROOM DIVIDER | EA | 01 | H= 06 FT, L= 20 FT, Material : Fabric, Frame Steel |
| 6 | 5844NL-7542005 | CONTROL CABLE S960CY 3-PHASE 5-CONDUCTOR | EA | 100 | Manufacturer : SAB North America or Equivalent Manufacturing Part No : 07542005 Voltage : 600V Conductor : 5, Gauge : 20 AWG Tinned Bried Shield Temperature Range : -5C TO +90C Copper Class : Class 6 Type : Continuous Flux Cable |
| 7 | 5844NL-7852603 | MULTI CONDUCTOR CABLE S960CY 1-PHASE 3-CONDUCTOR | EA | 200 | Manufacturer : SAB North America or Equivalent Manufacturing Part No : 07852603 Voltage : 300V Conductor : 3, Gauge : 26 AWG Tinned Braid Shield Temperature Range : -5C TO +80C Copper Class : Class 6 Type : Continuous Flux Cable |
| 8 | GS-18CITHI12G | DC INVERTOR AC 1.5 TON | EA | 2 | Manufacturer : GREE or Equivalent Manufacturing Part No : GS-18CITHI12G BTU Capacity : 1.5 Ton (18000 BTU) Low Voltage Startup : 150V Refrigerant : R140 A Gas Current : 9 Amp |

# 2.	TECHNICAL AND COMMERCIAL OFFERS FOR PURCHASE OF ABOVE MENTIONED ITEMS MAY BE SUBMITTED IN SEALED ENVELOPES TO MD APF PAC KAMRA ON “FOR” BASIS AND MAY BE DROPPED IN TENDER BOX NO. 02 PLACED AT MAIN GUARD ROOM APF BEFORE 1100 HRS ON 08 APRIL 2021. VALIDITY PERIOD OF QUOTATION MUST BE 120 DAYS MINIMUM AND WILL BE OPENED ON THE SAME DAY AT 1130 HRS IN THE OFFICE OF DEPUTY DIR LOG (S&A), APF, PAC KAMRA. EDD (EXPECTED DELIVERY DATE) AND WARRANTY MUST BE MARKED ON EACH QUOTATION.

NOTE:-    INTERESTED FIRMS ARE TO DEPOSIT BID SECURITY @ 5% OF QUOTE (NOT EXCEEDING 0.150 M) IN FAVOUR OF PUBLIC FUND ACCOUNT IN THE FORM OF CDR / PAY ORDER / DEMAND DRAFT ONLY WITH QUOTATION. WITHOUT BID SECURITY NO QUOTATION WILL BE CONSIDERED. CROSS CHEQUE WILL NOT BE ACCEPTED.

# 3.     THIS FACTORY RESERVES THE RIGHT TO REJECT ANY QUOTATION ON TECHNICAL GROUNDS. ONLY REGISTERED SUPPLIERS, WHO ARE ON ACTIVE TAXPAYERS LIST OF FBR ARE TO QUOTE AND SUBMIT DOCUMENTARY PROOF ALONGWITH TECHNICAL QUOTATIONS. THE ENVELOPE MUST CLEARLY MENTION “TENDER INQUIRY REF NO” TO DIRECTOR LOGISTICS APF. FURTHER DETAILS IF REQUIRED MAY BE OBTAINED FROM CONTACTNO. 051-90996358 ON FAX NO.051-9225514 OR VISIT PAC WEBSITE {www.pac.org.pk}.

(ABDUL WAJID NAZEER)

SQUADRON LEADER

FOR  MANAGING DIRECTOR

APF PAC KAMRA

Directorate of Logistic, APF, PAC Kamra                                    TEL EXT: 6292